## Slide 1: Simulation of a Production line
By: Pedro Rodriguez

## Slide 2: Problem
Production line is experiencing inconsistency in meeting the daily goal.
The focus will be the production line 5
The first 3 stations should produce 600 units

## Slide 3: Who might care?
Springboard Mentor
Manufacturing manager
Manufacturing Engineer
Process Engineer

## Slide 4: What factors can be affecting the process?
Supplier
Materials
Equipment
Process time
Available labor and human error

## Slide 5: Data Information
station | production_line | Cycle_time
1 | 1 | 96.20
2 | 1 | 22.20
3 | 2 | 7.25
4 | 2 | 11.67
5 | 2 | 75.25
station | station_no. | Downtime
station 1 | 1 | 2942
station 2 | 2 | 605
station 3 | 3 | 717
station 4 | 4 | 1014
station 5 | 5 | 1743
station | station_no. | Date | Downtime | Year
station 1 | 1 | 2018-01-01 | 8 | 2018
station 2 | 2 | 2018-01-01 | 8 | 2018
station 3 | 3 | 2018-01-01 | 4 | 2018
station 4 | 4 | 2018-01-01 | 7 | 2018
station 5 | 5 | 2018-01-01 | 6 | 2018

## Slide 6: Understanding the currently line
Takt time is the rate at which you need to complete a product to meet customer demand.
Total Available Production Time
Takt time =
Average Customer Demand
Takt time = 65.89 second per unit

## Slide 7: Downtime durations
The mean downtime duration is 24.11 minutes with a standard deviation of 11.91 minutes.
In every Downtime the lines are not producing an average of 21 units per station downtime.
More information is needed

## Slide 8: Downtime frequency
Ttest_indResult(
statistic=-14.61679464448569,
pvalue=8.912783594431311e-45)

## Slide 9: Simulation
Supplier
Station 1
Station 2
Station 3
Dispatch
56 units per hour
Mean: 17 sec
Std: 2 sec
Mean: 13 sec
Std: 3 sec
Mean: 16 sec
Std: 2 sec
600 units at the end of the shift
Facts:
Production line 4 should regularly supply 56 units per hour.
To have enough supply for the Production line six and seven to complete the daily goal, the production line 5 need the first three stations to produce 600 units.

## Slide 10: Simulation run
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 588 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 600 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 600 units processed
------------------------------
SIMULATION COMPLETED
First Run
Second Run
Third Run
Actual Process Parameter:
num_station_1 = 1
mean_station_1 = 17
std_station_1 = 2
num_station_2 = 1
mean_station_2 = 14
std_station_2 = 3
num_station_3 = 1
mean_station_3 = 16
std_station_3 = 2

## Slide 11: Simulation run Test #1
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 588 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 588 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 600 units processed
------------------------------
SIMULATION COMPLETED
First Run
Second Run
Third Run
Actual Process Parameter:
num_station_1 = 1
mean_station_1 = 17
std_station_1 = 1
num_station_2 = 1
mean_station_2 = 14
std_station_2 = 1
num_station_3 = 1
mean_station_3 = 16
std_station_3 = 1

## Slide 12: Simulation run Test #2
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 636 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 648 units processed
------------------------------
SIMULATION COMPLETED
STARTING SIMULATION
------------------------------
RUNNING TIME: 12 hours
------------------------------
Production line has 624 units processed
------------------------------
SIMULATION COMPLETED
First Run
Second Run
Third Run
Actual Process Parameter:
num_station_1 = 1
mean_station_1 = 17
std_station_1 = 1
num_station_2 = 1
mean_station_2 = 14
std_station_2 = 1
num_station_3 = 1
mean_station_3 = 16
std_station_3 = 1

## Slide 13: Future Improvement
In the future, I would like to spend more time with the simulation, adding more constrain to see how the process flow behaves.
Adding constraints helps determine which limitations significantly impact the line and support the management in maximizing the output.